## Slide 1: LKA Functional Safety Draft Presentation
Davide Occello, January 6th 2017

## Slide 2: Content
Introduction
Project Timeline
Euro NCAP Requirements
Functional Safety Concept (ISO 26262)
  Item Definition
  Safety Relevant Use Cases
  HARA & Safety Goals
  Functional Architecture
  Functional Safety Requirements
  Improved Architecture (Draft)
Deliverables

## Slide 3: Introduction
Why Active Lane Keeping Assist
The system aims to avoid dangerous situations like the following:
Driver distraction Late realisation of danger  panic responseloss of control crash
Approach to avoid the scenario
Support the driver by actively steering towards the center of the lane and warn him in advance if the car is going to close to the edge

## Slide 4
2016
2017
Today
Nov
Dec
Jan
Feb
Mar
Project Kick Off
25.11.16
Project End
28.03.17
25/11/16 – 13/01/17
Phase 1: Functional Safety
26 days
23 days
55 days
12 days
43 days
Phase 2:
Design
Phase 3: Implementation
13.01.17
16.01.17
27.01.17
30.01.17
Project Timeline

## Slide 5
2016
2017
Today
Nov
Dec
Jan
Project Kick Off
25.11.16
25/11/16 – 13/01/17
Phase 1:
Functional Safety
26 days
13.01.17
NCAP Requirements
2nd Dec
CAFCR
9th Dec
HARA
14th Dec
FSR
20th Dec
Documentation
12th Jan
End – Phase 1
Project Timeline (Phase 1)
Holidays

## Slide 6
EURO NCAP Requirements
This protocol specifies the Lateral Support Systems test procedure
Mainly information about the test conditions
Some Information on the other systems that are required in combination with the LKA
Suggestions on the operation of the system

## Slide 7
EURO NCAP Requirements
Examples from the document:
Test conditions: LKA should detect unintentional lane change at least, when the outside of the tire closest to the outside of the lane markings crosses 0.3 m or beyond.
System functionality: LKA shall use the lateral support system to restore control of the vehicle while countering the unintentional lane change.
Required Additional Systems: LKA system shall be available only if vehicle possess Electronic Stability Control system in compliance with regulatory requirements.

## Slide 8: Functional Safety Concept (ISO 26262)
Phase 1 of the project:
Item definition
HARA
FSC

## Slide 9: Item Definition
  The main system function of a ‘Lane Keeping Assistance System (LKAS)’ is:
  detect the unintentional drift outside the lane on which it is travelling
  to support the driver in keeping the vehicle within the current lane
  the responsibility for the safe operation of the vehicle always remains with the driver.
Approach to Functional Safety
Warn the Driver and deactivate LKA when failures occur
Add redundancy for very important functionalities

## Slide 10: Scenarios
Visual Representation
Safety Relevant Use Cases
Vehicle Speed
  Vv= 50 -130 kph (normal operating conditions)
Lateral vehicle acceleration < 0.3 g
Lane markings according to the EU road network legislation
Target Environment: Highway*
* Information derived from EURO NCAP requirement document

## Slide 11: Straight Lane /
Vv
Vout
10-30 cm
10-30 cm
10-20 cm
ε
3.5-3.7 m
R >1000 m
Expected Control Action

## Slide 12: Curve /
Vv
ε
Vout
R >250 m
Preferred Trajectory
Expected Control Action

## Slide 14: Traffic Jam (Vv<50 kph)
Vout
10-30 cm
10-30 cm
10-20 cm
ε
Vv

## Slide 15: Hazard and Risk Analysis

## Slide 16: Hazard and Risk Analysis

## Slide 17: Functional Architecture

## Slide 18: Functional Architecture

## Slide 19: Functional Architecture
Highly safety critical
ASIL D

## Slide 20: Improved Architecture
ASIL A (D)
ASIL C (D)
ASIL A (D)
ASIL C (D)
ASIL D
ASIL D
ASIL D
ASIL B (D)
ASIL C (D)
ASIL A (D)
Safety Measures
ASIL A (D)

## Slide 21: Improved Architecture (Unfinished)
ASIL C

## Slide 22: Questions
?