## Slide 1: LKA Functional Safety Draft Presentation
Davide Occello, January 6th 2017

## Slide 2: Content
Project Timeline
Euro NCAP Requirements
Functional Safety Concept (ISO 26262)
  Item Definition
  Safety Relevant Use Cases
  HARA & Safety Goals
  Functional Architecture
  Functional Safety Requirements
  Improved Architecture (Draft)
Deliverables

## Slide 3
2016
2017
Today
Nov
Dec
Jan
Feb
Mar
Project Kick Off
25.11.16
Project End
28.03.17
25/11/16 – 13/01/17
Phase 1: Functional Safety
26 days
23 days
55 days
12 days
43 days
Phase 2:
Design
Phase 3: Implementation
13.01.17
16.01.17
27.01.17
30.01.17
Project Timeline

## Slide 4
2016
2017
Today
Nov
Dec
Jan
Project Kick Off
25.11.16
25/11/16 – 13/01/17
Phase 1:
Functional Safety
26 days
13.01.17
NCAP Requirements
2nd Dec
CAFCR
9th Dec
HARA
14th Dec
FSR
20th Dec
Documentation
11th Jan
End – Phase 1
Project Timeline (Phase 1)

## Slide 5
EURO NCAP Requirements
Examples from the document:
Important functional requirements:
LKA: LKA should detect unintentional lane change at least, when the outside of the tire closest to the outside of the lane markings crosses 0.3 m or beyond.
  (source : Partially from EURO NCAP: section1 and UNECE)
LKA: LKA shall use the lateral support system to restore control of the vehicle while countering the unintentional lane change.
(source : EURO NCAP: section1)

## Slide 6: Functional Safety Concept (ISO 26262)

## Slide 7: Item Definition
  ‘One of the causes of lane road accidents is unintended lane departure during driving. The main system function of a ‘Lane Keeping Assistance System (LKAS)’ is to detect the unintentional drift outside the lane on which it is travelling and to support the driver in keeping the vehicle within the current lane. The system primarily uses camera sensor(s) to detect lane markings or makes use of available software like mobileye to get the lane markings. It also acquires the data and estimates the lateral position of the subject vehicle and when required, sends command(s) to the actuator(s) to influence the lateral movement of the vehicle. The intention of driver to leave a lane is detected by the toggling of the indicator/turn signal switch or by even measuring the torque applied on the steering wheel of the vehicle. The status information of LKAS can be provided to the driver by means of audio, visual or even haptic elements. LKAS is an assist feature and not an autonomous driving feature. The responsibility for the safe operation of the vehicle always remains with the driver. LKAS is intended here to be operated only on highways with forward driving speed more than 50 Kph. Temperatures outside -20 to 50 deg celsius band are considered out of scope for LKAS. Roads and lane markings outside Europe are considered out of scope here.’

## Slide 8: Scenarios
Visual Representation
Legend:
Sunny weather/Dry road conditions
Wet weather/Wet road conditions
Engine Off
Safety Relevant Use Cases

## Slide 9: Highway
Vehicle Speed
  Vv= 50 -130 kph (normal operating conditions)
  Vv= 0 -50 kph (traffic jam)
Lane departure speeds (Vout) =0.1 – 1 m/s
Lateral vehicle acceleration < 0.3 g
Lane markings according to the following slides
Ideal Road Conditions:
  Dry
  Horizontal visibility till 1km Ambient temperature between 5 to 40 deg.
  Natural ambient illumination excess of 2000 lux for day light with no strong shadow
  Uniform solid paved surface with consistent slope and no irregularity within a lateral distance of 3.0 m to either side. The minimum peak braking coefficient shall be 0.9
  Slope of the surface between 0 and 1 deg
Ideal Vehicle Conditions:
  Original fitment of tires according to make, model, size, speed and load rating specified by the manufacturer.
  Default wheel alignment measure set by the OEM
  Accuracy of the sensors according to EURO NCAP

## Slide 10: Straight Lane
Vv
Vout
10-30 cm
10-30 cm
10-20 cm
ε
3.5-3.7 m
R >1000 m
Expected Control Action

## Slide 11: Straight Lane
Vv
Vout
10-30 cm
10-30 cm
10-20 cm
ε
3.5-3.7 m
R >1000 m
Expected Control Action

## Slide 12: Curve
Vv
ε
Vout
R >250 m
Preferred Trajectory
Expected Control Action

## Slide 13: Curve
Vv
ε
Vout
R >250 m
Preferred Trajectory
Expected Control Action

## Slide 14: Overtaking/Lane Change
Vout
10-30 cm
10-30 cm
10-20 cm
ε
Vv

## Slide 15: Overtaking/Lane Change
Vout
10-30 cm
10-30 cm
10-20 cm
ε
Vv

## Slide 16: Traffic (Vv>50 kph)
Vout
10-30 cm
10-30 cm
10-20 cm
ε
Vv

## Slide 17: Traffic Jam (Vv<50 kph)
Vout
10-30 cm
10-30 cm
10-20 cm
ε
Vv

## Slide 18: Low visibility/Obstructed View
Horizontal Perspective
Bird’s Eye Perspective

## Slide 19: Poor road condition
Horizontal Perspective
Bird’s Eye Perspective

## Slide 20: Engine off (Vv>50 kph)
Vout
10-30 cm
10-30 cm
10-20 cm
ε
Vv

## Slide 21: Hazard and Risk Analysis
Example for the activation function

## Slide 22: Functional Architecture

## Slide 23: Functional Architecture

## Slide 24: Improved Architecture (Unfinished)

## Slide 25: Improved Architecture

## Slide 26: Questions
?